# Appendix 1A: R code and packages used

## A.1	Curve distances

library(TSdist)

## 1 week RT example , in this case read curves defined by 104 data .

curvas <− read.csv(“...”)

t_curvas<-t(curvas)

# direction distance, Cosine dissimilarity matrix

cdiss<−as.matrix (dist (t_curvas,method = “cosine”))

rad2deg <− function(rad){(rad∗180)/(pi)}

cdiss.rad<−rad2deg(cdiss)

# magnitude distance

magnitude<−as.matrix(dist(t_curvas))

# Keep in the distance o f each curve to the average curve (Rc )

dif_resp_ref  <−t(t(data.frame(magnitude[“R c”,] , cdiss.rad[“R c”,])))

A.2	Regression model

# Read the table of Variogram parameters adjusted via a spherical model at each TR.

variog_range_resTemp <− read.csv(“...” ) SampFreq<− 1/TR

# scatterplot

scatter.smooth ( x= SampFreq , y= Range , main=” Sampling frequency~Range” ,

xlab = “Sampling frequency” ,

ylab= “Range of spatial autocorrelation” )

# Linear model

linearMod <− lm( Range ~ SampFreq )

summary( linearMod )

## Polar plot

library(”plotrix”)

radial.labels<−function(lengths,radial.pos , units=”radians” , start =0 , clockwise=FALSE,

labels , adj=NULL, pos=NULL,...){

i f (units == “clock24” ) radial.pos<−p i ∗(450 − radial.pos∗ 15 ) /180

i f (units == “polar” ) radial.pos<−pi∗radial.pos/180

if(clockwise)radial.pos<− radial.pos if(start)radial.pos<−radial.pos+start

#get the vector of x positions

xpos<−cos(radial.pos)∗lengths

# get the vector of y positions

ypos<−sin(radial.pos) ∗ lengths

text( xpos , ypos , labels , adj=adj , pos=pos,...)

}

polar.plot(dif_resp_ref[ , 1 ] , dif_resp_ref[ , 2 ] ,

rp . type = ” dots ” , show . grid . labels=FALSE,

point . symbols=”” ,  point . col  =  ” red ” ,  start=  0 , clockwise = FALSE, main=”1w” )

r a d i a l . labels (dif_resp_ref[ , 1 ] , dif_resp_ref[ , 2 ] ,

u n i t s ="polar ” , labels = c (rownames(dif_resp_ref) ) ,

col ="red”)

## Weighted network

library( qgraph )

# Lat Lon coordinates

xy<−read . csv (“coordinateslat.csv”) xymat<−as.matrix ( xy [ , 2 : 3 ] )

## Euclidean Distance

eucli<−TS Database Distances ( t curvas ,  distance="euclidean”)

eucli.ma<−as.matrix(eucli)

disteu<− 1/eucli.ma

# one over , as qgraph takes similarity matrices as input

#Weighted network

qgraph (disteu , layout=xymat )